DESCRIPTION

PASSION 2T TOURING is a lubricant with very low exhaust smoke levels for the latest generation of two-stroke engines of scooters. It is formulated with special synthetic components which make it particularly suitable for use in both air-and water-cooled engines.

# PASSION 2T TOURING although formulated specifically for oil injection systems, can be used for premix mixtures as well. The product can also be employed in mixtures with unleaded gasoline.

PROPERTIES AND PERFORMANCES

PASSION 2T TOURING minimises deposit formation in the combustion chamber, the ring area and the exhaust system, while reducing spark-plug fouling and ensuring that the components remain clean.

Careful selection of the synthetic base results, in very low exhaust smoke levels.

The product has superior “self-mixing” properties thus guaranteeing very rapid mixing with the gasoline, for use on engines fitted with oil injection systems.

PASSION 2T TOURING  provides excellent protection against engine corrosion, rust and wear.

CHARACTERISTICS

Viscosity at 100°C			mm²/s			11.8

Viscosity at 40°C			mm²/s			94

Viscosity Index			C			115

Pour Point				°C			-24

Flash Point C.O.C.			°C			125

Mass. Density at 15°C		kg/L			0.874

SPECIFICATIONS

PASSION 2T TOURING meets the requirements of the following specifications:

- API TC

- JASO FC